## Slide 1: GALAMSEY IMPACT ON WATER POLLUTION
Using Data to Expose Environmental Damage and Inform Action

## Slide 2: Introduction
This project investigates the impact of illegal mining (galamsey) on water bodies in Ghana.
By analyzing river water samples from galamsey-affected regions, the project uncovers serious health and environmental risks caused by heavy metal contamination and poor water quality.

## Slide 3: Key Water Quality Indicators
pH: Indicates water acidity (ideal range: 6.5–8.5)
Heavy Metals: Arsenic (As), Cadmium (Cd), Chromium (Cr), Lead (Pb)
TDS (Total Dissolved Solids): Measures mineral content
Conductivity: Indicates ionic concentration
Water Hardness: Levels of Calcium and Magnesium

## Slide 4: Dashboard Walk Through
Software Used: Microsoft Power BI
Dashboard breakdown
  WATER POLLUTANTS DASHBOARD
  STANDARDS COMPARISON DASHBOARD
  WATER QUALITY DASHBOARD
  GALAMSEY IMPACT DASHBOARD

## Slide 5: Findings: Galamsey Pit Sample
Extremely low pH (3.21), highly acidic and unsafe
Arsenic: 3.56 mg/L | Chromium: 3.35 mg/L | Lead: 1.15 mg/L | Cadmium: 0.01 mg/L
All values exceed WHO safe limits for drinking water
Indicates severe chemical leaching from illegal mining

## Slide 6: Widespread Pollution Across Rivers
Multiple rivers downstream from galamsey zones show:
Acidic pH values (as low as 5.25)
High TDS and conductivity levels
Unsafe concentrations of heavy metals
Indicates large-scale environmental impact

## Slide 7: Call to Action
This visualization is more than data—it is a call to action:
  Empower communities to monitor their water
  Advocate for enforcement of mining regulations
  Promote ecological restoration of damaged river systems
  Support sustainable alternatives to illegal mining

## Slide 8: Acknowledgments
Prepared by: Elvis Kwabena Asare Nkrumah
For: Galamsey Data Visualization Hackathon 2025
Organized by: Open Data Bank Ghana